## Slide 1: 21CSS201T COMPUTER ORGANIZATION AND ARCHITECTURE UNIT-1

## Slide 2: Computer Architecture Objectives
Know the difference between computer organization and computer architecture.
Understand units of measure common to computer systems
Appreciate the evolution of computers.
Understand the computer as a layered system.
Be able to explain the von Neumann architecture and the function of basic computer components.

## Slide 3: COMPUTER ARCHITECTURE AND ORGANIZATION OVERVIEW
A modern computer is an electronic, digital, general purpose computing machine that automatically follows a step-by-step list of instructions to solve a problem. This step-by step list of instructions that a computer follows is also called an algorithm or a computer program.
Why to study computer organization and architecture?
  Design better programs, including system software such as compilers, operating systems, and device drivers.
  Optimize program behavior.
  Evaluate (benchmark) computer system performance.
  Understand time, space, and price tradeoffs.
Computer organization
  Encompasses all physical aspects of computer systems.
  E.g., circuit design, control signals, memory types.
  How does a computer work?

## Slide 4
Focuses on the structure(the way in which the components are interrelated) and behavior of the computer system and refers to the logical aspects of system implementation as seen by the programmer
Computer architecture includes many elements such as
  instruction sets and formats, operation codes, data types, the number and types of registers, addressing modes, main memory access methods, and various I/O mechanisms.
The architecture of a system directly affects the logical execution of programs.
The computer architecture for a given machine is the combination of its hardware components plus its instruction set architecture (ISA).
The ISA is the interface between all the software that runs on the machine and the hard
Studying computer architecture helps us to answer the question: How do I design a computer?
COMPUTER ARCHITECTURE AND ORGANIZATION OVERVIEW

## Slide 5
In the case of the IBM, SUN and Intel ISAs, it is possible to purchase processors which execute the same instructions from more than one manufacturer
All these processors may have quite different internal organizations but they all appear identical to a programmer, because their instruction sets are the same
Organization & Architecture enables a family of computer models
Same Architecture, but with differences in Organization
Different price and performance characteristics
When technology changes, only organization changes.
This gives code compatibility (backwards)
COMPUTER ARCHITECTURE AND ORGANIZATION OVERVIEW

## Slide 6: COMPUTER COMPONENTS
At the most basic level, a computer is a device consisting of 3 pieces
  A processor to interpret and execute programs
  A memory ( Includes Cache, RAM, ROM) to store both data and program instructions
  A mechanism for transferring data to and from the outside world.
    I/O to communicate between computer and the world
    Bus to move info from one computer component to another

## Slide 7: Contd..
Computers with large main memory capacity can run larger programs with greater speed than computers having small memories.
RAM is an acronym for random access memory. Random access means that memory contents can be accessed directly if you know its location.
Cache is a type of temporary memory that can be accessed faster than RAM.

## Slide 8: Digital System
Takes a set of discrete information inputs and discrete internal information (system state) and generates a set of discrete information outputs.
System State
Discrete
Information
Processing
System
Discrete Inputs
Discrete
outputs

## Slide 9: Signal
An information variable represented by physical quantity.
For digital systems, the variable takes on discrete values.
Two level, or binary values are the most prevalent values in digital systems.
Binary values are represented abstractly by:
  digits 0 and 1
  words (symbols) False (F) and True (T)
  words (symbols) Low (L) and High (H)
  and words On and Off.
Binary values are represented by values or ranges of values of physical quantities

## Slide 10: Introduction to Number System and Logic Gates
  Number Systems- Binary, Decimal, Octal, Hexadecimal
  Codes- Grey, BCD,Excess-3,
  ASCII, Parity
  Binary Arithmetic- Addition, Subtraction, Multiplication, Division using Sign Magnitude
  1’s complement, 2’s complement,
  BCD Arithmetic;
  Logic Gates-AND, OR, NOT, NAND,
  NOR, EX-OR, EX-NOR

## Slide 30: BINARY ARITHMETIC

## Slide 34: Signed Binary Numbers
Two ways of representing signed numbers:
  1) Sign-magnitude form, 2) Complement form.
Most of computers use complement form for negative number notation.
1’s complement and 2’s complement are two different methods in this type.

## Slide 35: 1’s Complement
1’s complement of a binary number is obtained by subtracting each digit of that binary number from 1.
Example
Shortcut: Invert the numbers from 0 to 1 and 1 to 0

## Slide 36: 2’s Complement
2’s complement of a binary number is obtained by adding 1 to its 1’s complement.
Example
Shortcut: Starting from right side, all bits are same till first 1 occurs and then invert rest of the bits

## Slide 37: Subtraction using 1’s complement
Using 1’s complement
  Obtain 1’s complement of subtrahend
  Add the result to minuend and call it intermediate result
  If carry is generated then answer is positive and add the carry to Least Significant Digit (LSD)
  If there is no carry then answer is negative and take 1’s complement of intermediate result and place negative sign to the result.

## Slide 38: Subtraction using 2’s complement
Using 2’s complement
  Obtain 2’s complement of subtrahend
  Add the result to minuend
  If carry is generated then answer is positive, ignore carry and result itself is answer
  If there is no carry then answer is negative and take 2’s complement of intermediate result and place negative sign to the result.

## Slide 39: Subtraction using 1’s complement (Examples)
Example - 1

## Slide 40: Subtraction using 1’s complement (Examples)
Example - 2

## Slide 41: Subtraction using 2’s complement (Examples)
Example - 1

## Slide 42: Subtraction using 2’s complement (Examples)
Example - 2

## Slide 43: BCD ARITHMETIC

## Slide 44: BCD Addition
Example - 1
Rule: If there is an illegal code or carry is generated as a result of addition, then add 0110 to particular that 4 bits of result.

## Slide 45: BCD Addition
Example - 2

## Slide 46: BCD Subtraction
Example - 1
Rule: If one 4-bit group needs to take borrow from neighbor, then subtract 0110 from the group which is receiving borrow.

## Slide 47: BCD Subtraction
Example - 2

## Slide 50: GRAY CODE
Gray code is the arrangement of binary number system such that each incremental value can only differ by one bit.
This code is also known as Reflected Binary Code (RBC), Cyclic Code and Reflected Binary (RB). The reason for calling this code as reflected binary code is the first N/2 values compared with those of the last N/2 values in reverse order.
In gray code when transverse from one step to another step the only one bit will be change of the group. This means that the two adjacent code numbers differ from each other by only one bit.
It is popular for unit distance code but it is not use from arithmetic operations. This code has some application like convert analog to digital, error correction in digital communication.

## Slide 51: Binary- Gray code conversion
STEPS
  The most significant bit of gray code is equal to the first bit of the given binary bit.
  The second bit of gray code will be exclusive-or (XOR) of the first and second bit of the given binary bit.
  The third bit of gray code is equal to the exclusive-or (XOR) of the second and third binary bits. For father gray code result this process will be continuing.

## Slide 52: Explanation
Truth Table of XOR |  | 
A | B | C
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
The given binary digit is 01001

## Slide 53: Example
The gray code of the given binary code is (010.01)2 ??
  The first MSB bit of binary is same in the first bit of gray code. In this example the binary bit is “0”. So, gray bit also “0”.
  Next gray bit is equal to the XOR of the first and the second binary bit. The first bit is 0, and the second bit is 1. The bits are different so resultant gray bit will be “1” (second gray codes bit)
  The XOR of the second and third binary bit. The second bit is 1 and third is 0. These bits are again different so the resultant gray bit will be 1 (third gray codes bit)
  Next we perform the XOR operation on third and fourth binary bit. The third bit is 0, and the fourth bit is 0. The both bits are same than resultant gray codes will be 0 (fourth gray codes bit).
  Take the XOR of the fourth and fifth binary bit. The fourth bit is 0 and fifth bit is 1. These bits are different than resultant gray codes will be 1 (fifth gray code bit)
  The result of binary to gray codes conversion is 01101.

## Slide 54
You can convert n bit (bnb(n-1)…b2b1b0) binary number to gray code (gng(n-1)…g2g1g0). For most significant bit bn=gn, and rest of the bit by XORing b(n-1)=g(n-1)⊕gn, ….

## Slide 55: GRAY CODE TABLE The conversion in between decimal to gray and binary to gray code is given below
Decimal Number | Binary Number | Gray Code
0 | 0000 | 0000
1 | 0001 | 0001
2 | 0010 | 0011
3 | 0011 | 0010
4 | 0100 | 0110
5 | 0101 | 0111
6 | 0110 | 0101
7 | 0111 | 0100
8 | 1000 | 1100
9 | 1001 | 1101
10 | 1010 | 1111
11 | 1011 | 1110
12 | 1100 | 1010
13 | 1101 | 1011
14 | 1110 | 1001
15 | 1111 | 1000
:
The gray code of the given binary code
(01001) =0 1 1 0 1. We can see one bit change in the next incremental value.

## Slide 56: Gray-Binary code conversion
STEPS
  The most significant bit of gray codes is equal in binary number.
  Now move to the next gray bit, as it is 1 the previous bit will be alter i.e it will be 1, thus the second binary bit will be 1.
  Next see the third bit, in this example the third bit is 1 again, the third binary bit will be alter of second binary bit and the third binary bit will be 0.
  Now fourth bit of the, here the fourth bit of gray code is 0. So the fourth bit will be same as a previous binary bit, i.e 4th binary bit will be 0.
  The last fifth bit of gray codes is 1; the fifth binary number is altering of fourth binary number.
  Therefore the gray code (01101) equivalent in binary number is (01001)

## Slide 57: Explanation
The given gray code is 01101
0 1 1 0 1 (Gray)
MSB
LSB
Binary code Conversion
Truth Table of XOR |  | 
A | B | C
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 58: Merits & Demerits of Gray Code
Advantages of gray code
It is best for error minimization in conversion of analog to digital signals.
It is best for minimize a logic circuit
Decreases the “Hamming Walls” which is undesirable state, when used in genetic algorithms
It is useful in clock domain crossing
Disadvantages of gray code
Not suitable for arithmetic operations
It has limited use.

## Slide 59: Binary Codes for Decimal Digits
Decimal
8,4,2,1
Excess3
8,4,
-
2,
-
1
Gray
0
0000
0011
0000
0000
1
0001
0100
0111
0100
2
0010
0101
0110
0101
3
0011
0110
0101
0111
4
0100
0111
0100
0110
5
0101
1000
1011
0010
6
0110
1001
1010
0011
7
0111
1010
1001
0001
8
1000
1011
1000
1001
9
1001
1
100
1111
1000
There are over 8,000 ways that you can chose 10 elements from the 16 binary numbers of 4 bits. A few are useful:

## Slide 60: Binary Coded Decimal (BCD)
The BCD code is the 8,4,2,1 code.
This code is the simplest, most intuitive binary code for decimal digits and uses the same powers of 2 as a binary number, but only encodes the first ten values from 0 to 9.
Example: 1001 (9) = 1000 (8) + 0001 (1)
How many “invalid” code words are there?
What are the “invalid” code words?
Notes: Answer 1: 6
Answer 2: 1010, 1011, 1100, 1101, 1110, 1111

## Slide 61: Excess 3 Code and 8, 4, –2, –1 Code
What interesting property is common to these two codes?
Decimal | Excess 3 | 8, 4, –2, –1
0 | 0011 | 0000
1 | 0100 | 0111
2 | 0101 | 0110
3 | 0110 | 0101
4 | 0111 | 0100
5 | 1000 | 1011
6 | 1001 | 1010
7 | 1010 | 1001
8 | 1011 | 1000
9 | 1100 | 1111
Notes: Answer: Both of these codes have the property that the codes for 0 and 9, 1 and 8, etc. can be obtained from each other by replacing the 0’s with the 1’s and vice-versa in the code words. Such a code is sometimes called a complement code.

## Slide 62: Decimal to BCD

## Slide 63: Binary to BCD conversion

## Slide 64: Advantages of BCD
  Easy to encode and Decode decimals into BCD and Vice-versa
  Easy to implement a hardware algorithm for BCD converter
  Very useful in digital systems whenever decimal information reqd.
  Digital voltmeters, frequency converters and digital clocks all use BCD as they display output information in decimal.

## Slide 65: Disadvantages of BCD Code
  Require more bits than straight binary code
  Difficult to be used in high speed digital computer when the size and capacity of their internal registers are restricted or limited.
  The arithmetic operations using BCD code require a complex design of Arithmetic and Logic Unit (ALU) than the straight binary number system.
  The speed of the arithmetic operations that can be realized using BCD code is naturally slow due to the complex hardware circuitry involved.

## Slide 66: Excess-3 code
The excess-3 code is also treated as XS-3 code. The excess-3 code is a non-weighted and self-complementary BCD code used to represent the decimal numbers.
This code has a biased representation. This code plays an important role in arithmetic operations because it resolves deficiencies encountered when we use the 8421 BCD code for adding two decimal digits whose sum is greater than 9.
The Excess-3 code uses a special type of algorithm, which differs from the binary positional number system or normal non-biased BCD.

## Slide 67: Decimal to Excess-3 code conversion
Step-1: We find the decimal number of the given binary number. Step-2: Then we add 3 in each digit of the decimal number.
Step-3: Now, we find the binary code of each digit of the newly generated decimal number.
Alternatively,
We can also add 0011 in each 4-bit BCD code of the decimal number for getting excess-3 code.

## Slide 68: Ex-1

## Slide 69: Ex-2

## Slide 70: Ex-3

## Slide 71: Excess-3 code

## Slide 72: Ex-4
Decimal | BCD
8 | 1000
1 | 0001
6 | 0110
1 | 0001
BCD+ 0011 | Excess-3
1000+0011 | 1011
0001+0011 | 0100
0110+0011 | 1001
0001+0011 | 0100

## Slide 73: Ex 5
Convert (11110)2 to Excess-3 using binary
Step 1: Convert binary to Decimal. (11110)2 = (30)10
Step 2: Add ‘3’ to individual digits to decimal number
3 0
3 3
6 3
Step 3: Find binary values of (63)10 = (01100011)Excess-3

## Slide 74: Ex 6
Convert (01100011) Excess-3 to binary.
Step- 1 : Find the decimal by dividing it four digits
  (01100011) Excess-3 = (0110 0011) Excess-3 = (30) 10
Step-2 : Find the binary value of the decimal through division method.
(01100011) Excess-3 = (11110)2

## Slide 75: Advantages
These codes are self-complementary.
These codes use biased representation.
The excess-3 code has no limitation, so that it considerably simplifies arithmetic operations.
The codes 0000 and 1111 can cause a fault in the transmission line. The excess-3 code doesn't use these codes and gives an advantage for memory organization.
These codes are usually unweighted binary decimal codes.
This code has a vital role in arithmetic operations. It is because it resolves deficiencies which are encountered when we use the 8421 BCD code for adding two decimal digits whose sum is greater than 9.

## Slide 76: ASCII
The ASCII stands for American Standard Code for Information Interchange. The ASCII code is an alphanumeric code used for data communication in digital computers.
The ASCII is a 7-bit code capable of representing 27 or 128 number of different characters. The ASCII code is made up of a three-bit group, which is followed by a four-bit code.

## Slide 77: ASCII Characters
Control Characters-0 to 31 and 127
Special Characters- 32 to 47, 58 to 64, 91 to 96, and 123 to 126
Numbers Characters- 0 to 9
Letters Characters - 65 to 90 and 97 to 122

## Slide 78: Ex 1
Encode (10010101100001111011011000011010100111000011011111101001 110111011101001000000011000101100100110011)2 to ASCII.

## Slide 79
Step 1:
The given binary data is grouped into 7-bits because the ASCII code is 7 bit.
1001010 1100001 1110110 1100001 1010100 1110000 1101111 1101001 1101110 1110100 1000000 0110001 0110010 0110011
Step 2:
Then, we find the equivalent decimal number of the binary digits either from the ASCII table or 64 32 16 8 4 2 1 scheme.

## Slide 80: Cont’d
Binary | 64 | 32 | 16 | 8 | 4 | 2 | 1 | DECIMAL | ASCII
1100011 | 1 | 1 | 0 | 0 | 0 | 1 | 1 | 99 | C
1101111 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 111 | O
1101101 | 1 | 1 | 0 | 1 | 1 | 0 | 1 | 109 | M
1110000 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 112 | P
1110101 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 117 | U
1110100 | 1 | 1 | 1 | 0 | 1 | 0 | 0 | 116 | T
1100101 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | 101 | E
1110010 | 1 | 1 | 1 | 0 | 0 | 1 | 0 | 114 | R
So the given binary digits results in ASCII Keyword COMPUTER

## Slide 81: Parity Code
The parity code is used for the purpose of detecting errors during the transmission of binary information. The parity code is a bit that is included with the binary data to be transmitted.
The inclusion of a parity bit will make the number of 1’s either odd or even. Based on the number of 1’s in the transmitted data, the parity code is of two types.
  Even parity code
  Odd parity code

## Slide 82
In even parity, the added parity bit will make the total number of 1’s an even number.
If the added parity bit make the total number of 1’s as odd number, such parity code is said to be odd parity code.

## Slide 83: Explanation

## Slide 84
On the receiver side, if the received data is other than the sent data, then it is an error. If the sent date is even parity code and the received data is odd parity, then there is an error.
So, both even and odd parity codes are used only for the detection of error and not for the correction in the transmitted data. Even parity is commonly used and it has almost become a convention.

## Slide 85: Logic Gates
Goal:
To understand how digital a computer can work, at the lowest level.
To understand what is possible and the limitations of what is possible for a digital computer.

## Slide 86: Logic Gates
All digital computers for the past 50 years have been constructed using the same type of components.
These components are called logic gates.
Logic gates have been implemented in many different ways.
Currently, logic gates are most commonly implemented using electronic VLSI transistor logic.

## Slide 87: Logic Gates
A logic gate is a simple switching circuit that determines whether an input pulse can pass through to the output in digital circuits.
The building blocks of a digital circuit are logic gates, which execute numerous logical operations that are required by any digital circuit.
These can take two or more inputs but only produce one output.
The mix of inputs applied across a logic gate determines its output. Logic gates use Boolean algebra to execute logical processes.
Logic gates are found in nearly every digital gadget we use on a regular basis.
Logic gates are used in the architecture of our telephones, laptops, tablets, and memory devices.

## Slide 88
All basic logic gates have the ability to accept either one or two input signals (depending upon the type of gate) and generate one output signal.
Logic Gates

## Slide 89: Truth Table
The outputs for all conceivable combinations of inputs that may be applied to a logic gate or circuit are listed in a truth table.
When we enter values into a truth table, we usually express them as 1 or 0, with 1 denoting True logic and 0 denoting False logic.

## Slide 90: Classification

## Slide 91
Basic Logic Gates-
Basic Logic Gates are the fundamental logic gates using which
universal logic gates and other logic gates are constructed.
They have the following properties-
Basic logic gates are associative in nature.
Basic logic gates are commutative in nature.
There are following three basic logic gates-
AND Gate
OR Gate
NOT Gate

## Slide 92: AND gate
The output of AND gate is high (‘1’) if all of its inputs are high (‘1’).
The output of AND gate is low (‘0’) if any one of its inputs is low (‘0’).

## Slide 93: OR Gate
The output of OR gate is high (‘1’) if any one of its inputs is high (‘1’).
The output of OR gate is low (‘0’) if all of its inputs are low (‘0’).
Logic Symbol-
The logic symbol for OR Gate is as shown below-

## Slide 94: NOT Gate
The output of NOT gate is high (‘1’) if its input is low (‘0’).
The output of NOT gate is low (‘0’) if its input is high (‘1’).
From here-
It is clear that NOT gate simply inverts the given input.
Since NOT gate simply inverts the given input, therefore it is also known as Inverter Gate.

## Slide 95: Universal Logic Gates
Universal logic gates are the logic gates that are capable of implementing any Boolean function without requiring any other type of gate.
They are called as “Universal Gates” because-
They can realize all the binary operations.
All the basic logic gates can be derived from them.
They have the following properties-
Universal gates are not associative in nature.
Universal gates are commutative in nature.

## Slide 96
A NAND Gate is constructed by connecting a NOT Gate at the output terminal of the AND Gate.
The output of NAND gate is high (‘1’) if at least one of its inputs is low (‘0’).
The output of NAND gate is low (‘0’) if all of its inputs are high (‘1’).
NAND GATE

## Slide 97: NOR Gate
A NOR Gate is constructed by connecting a NOT Gate at the output terminal of the OR Gate.
The output of OR gate is high (‘1’) if all of its inputs are low (‘0’).
The output of OR gate is low (‘0’) if any of its inputs is high (‘1’).

## Slide 98: EX-OR
An XOR gate (also known as an EOR, or EXOR gate) – pronounced as “Exclusive OR gate” – is a digital logic gate that gives a true (i.e. a HIGH or 1) output when the number of true inputs is odd.
An XOR gate implements an exclusive OR, i.e., a true output result occurs if one – and only one – of the gate’s inputs is true. If both inputs are false (i.e. LOW or 0) or both inputs are true, the output is false.

## Slide 99: EX-NOR
The XNOR gate (also known as an XORN’T, ENOR, EXNOR or NXOR) – and pronounced as Exclusive NOR – is a digital logic gate whose function is the logical complement of the exclusive OR gate (XOR gate). Logically, an XNOR gate is a NOT gate followed by an XOR gate.
The XOR operation of inputs A and B is A ⊕ B; therefore, the XNOR operation of those inputs will be (A + B) ̅. That means the output of the XOR gate is inverted in the XNOR gate.

## Slide 100: Example
Example 1
Q = A AND (B AND C)
Step 1 – Start with the brackets, this is the “B AND C” part.
Step 2 – Add the outer expression, this is the “A AND” part.

## Slide 101: Example
Example 2.
Q = NOT (A OR B)
Step 1 – Start with the brackets, this is the “A OR B” part
Step 2 – Add the outer expression, this is the “NOT” part.